## L10 WINDOWS/ ROOFLIGHTS/ SCREENS/ LOUVRES

To be read with Preliminaries/General conditions.

# TYPE(S) OF SYSTEM/EQUIPMENT

L10/45  ROOFLIGHT COVERS

Location: Insert here

Manufacturer and reference: Latchways Fall Protection plc, Hopton Park, Devizes, Wiltshire, SN10 2JP

- Ref: L10/45 Walksafe® Roof-light cover/protector System.

- System to be CE marked and hold EC Declarations of Conformity.

- Walksafe® Roof-Light Covers
Latchways manufacture Walksafe Roof-Light Covers designed to prevent the potential for falling through roof-lights when access across a non-fragile roof is required within 2 metres of the roof light.

- The Walksafe Roof-Light Covers are manufactured from PVC-U planks bolted to a 50mm chambered bearer.

- Walksafe Roof-Light Covers can be supplied to fit any type of roof light.

- The covers can be unclipped when a roof light requires cleaning.

- The covers are designed to allow the bearers to span across a minimum of two purlins and are tested on the assumption that the roof light will not absorb any of the loads during a fall.

- The covers must be designed to cover the roof light plus a minimum of 300mm overhang on each edge.

- Consult Latchways Plc. for technical literature or details. Latchways Plc. can also provide a design and specification advisory on the most appropriate walkway solution for each specific application and it is recommended that they are consulted early in the design process.

Other requirements: Rooflight cover / protector.
Manufacturer: Latchways Plc. Hopton Park, Devizes, Wiltshire SN10 2JP  Tel: 01380 732 700. Fax: 01380 732 701. Email: info@latchways.com Web: www.latchways.com 
Product reference: Walksafe Roof-Light Cover
Material: PVC-U planks
Colour: Consult with Latchways for details and samples.
Finish as delivered: Self finished