## H31 METAL PROFILED/ FLAT SHEET CLADDING/ COVERING

To be read with Preliminaries/General conditions.

# TYPE(S) OF SYSTEM/EQUIPMENT

# 120	Metal Roof Walkway

Latchways Roof Walkway and Access Systems

Latchways have worked with the major roofing manufacturers to produce a range of anti-slip walkways for:

- Standing seam roofing systems
- Membrane roofing systems
- Composite panel roofing systems
- Built-up metal roofing systems
- Secret fix roofing systems

WalkSafe is designed to provide a levelled, anti-slip, delineated walkway surface and affixes to the roof surface in a non-penetrative manner. It is available in 3 configurations:

- Levelled to falls
- Stepped
- Facetted

Latchways WalkSafe has been awarded Agrément Certificate No 99/3608.

The Health and Safety Executive recommends a minimum width of 430mm, or 600mm if materials are to be carried along a walkway.

Standing Seam Roofing Systems
Latchways has developed the modular WalkSafe walkway with anti-slip surface, for use on standing seam roofing systems.

The bespoke fixing kit supplied by Latchways allows non-penetrative fixing of the walkway panels. Designed to be used across the seams at an angle up to 6 degrees before levelling is required and up to 15 degrees running parallel to the seams.

The walkway can also be supplied levelled for use in situations where the roof pitch is greater than 6 degrees and in a step format when required to be running up or down a roof slope greater than 15 degrees.

Consult Latchways Plc. technical literature for details. Latchways can also provide a design and specification advisory on the most appropriate walkway solution for each specific application and it is recommended that they are consulted early in the design process.

Additional requirements:

Roof access walkway:
Manufacturer: Latchways plc., Hopton Park, Devizes Wiltshire SN10 2JP Tel: +44 (0)1380 732700 Fax: +44 (0)1380 732701 E-mail: spec@latchways.com Web: www.latchways.com 
Product reference: Latchways WalkSafe and Access System
Components:
Walkway surface: Anti-slip PVC-U planks
Colour: White / Brown / Silver Grey

Support members: 50mm PVC-U cushion bearers.
Fixing: Kalzip Standing Seam non-penetrative fixing clamp